## Slide 1
Mapping Exposures and Cumulative Risk of Hazardous Air Pollutants in the United States
1 Mariana Alifa Kassien*, 1 Kyle P. Messier
1 Predictive Toxicology Branch, Division of Translational Toxicology, National Institute of Environmental Health Sciences, Durham, United States
Pollutant | 2021 Sites | Mean MDL | % Non-Detects | % Below MDL | Mean days/site
Benzene | 282 | 0.21 | 2.2 | 8.9 | 97
Carbon tetrachloride | 226 | 0.30 | 3.2 | 25.8 | 46
Chloroform | 225 | 0.24 | 21.0 | 32.8 | 46
Hexane | 165 | 0.05 | 3.6 | 2.1 | 119
Map HAPs concentrations in the United States for recent years
Use novel statistical and computational methods for large datasets in multivariate scenarios and missing/censored data
Develop an analysis pipeline for easy reproducibility and expansion
Project Objectives
Hazardous Air Pollutants (HAPs)
Multivariate, Penalized, Land-Use Regression Model
Initial study: 4 HAPs, 2021
Preliminary results
188 compounds designated by EPA since 1990
EPA regulates HAPs emissions, but unlike criteria pollutants there are no ambient concentration standards regarding HAPs exposure
The HAPs database combines monitoring data collected by multitude entities: the EPA , other federal, sate, local, and tribal agencies, and other academic, community, and short-term studies
Extensive toxicology data on HAPs adverse effects: cancer, reproductive effects, and birth defects, among others
Need for more exposure and epidemiology studies to understand public health impacts of HAPs
Selection criteria:
Included in Tox21 database
33% or less non-detects
150 or more sites
~50% or more measurements above Min.Detection Limit (MDL)
Site locations 2021
Dataset challenges:
1. Sparsity in both space and time: few sites, most not sampled daily
2. Inhomogeneous sampling methods and frequency: data combined from different agencies
3. Censored data at sub-daily measurement scales: need special considerations for daily average computation (censored MLE)
4. Diversity of chemical classes: variety of effects of chemistry, physics, sources, and health effects
5. Computationally complex modeling: simultaneous fitting for multiple HAPs and a large number of covariates
Expanding to 2018-2021
Implementing analysis pipeline
Incorporating more covariates: meteorology, emissions, land use, seasons, etc.
Health impacts and exposure disparities research
Conclusions
We modeled the concentrations of four HAPs in the CONUS for 2021
We used a small initial set of data and covariates to conceptualize the analysis pipeline
Preliminary results show areas for improvement:
  Heterogeneity in validation results  investigate data outliers and rethink cross-validation methods
  Noisy model fit and predictions  addition of relevant covariates will allow for improvements across chemicals
Analysis pipeline development will streamline the expansion of this initial study, increasing computational efficiency and reducing user error
Land-use regression between pollutants z and covariates X:
Spatiotemporally correlated residuals
Expressed as Multivariate Gaussian density:
To solve, we need to optimize the objective function:
density
penalty
Problem: evaluation of covariance matrix takes time for each  computationally infeasible
Solution: use sparse approximation obtained through Sparse General Vecchia Approximation
(Messier and Katzfuss, 2021)
Spatial block cross-validation (5 –fold)
MSE results across all outcomes (μg/m3): 5, 26, 0.8, 75, 2
Mean MSE across CV-folds: 22 μg/m3
Validation metrics
Parameters selected
Prediction maps
Covariates from Gridmet (~4km reanalysis product).
Future covariates: more meteorology, emissions inventories (TRI, NEI), land use (OpenLandMap), etc.
Concentration (μg/m3)
Concentration (μg/m3)
Concentration (μg/m3)
Future Work:
Scan QR code for contact, related publications, and more!
References:
Bair E, Kidd B, Wimberley E, Mav D, Messier K (2024). PrestoGP: Penalized Regression for Spatio-Temporal Outcomes via Gaussian Processes. R package version 0.2.0.9036, https://niehs.github.io/PrestoGP/.
Climate and Health Outcomes Research Data System (CHORDS). https://www.niehs.nih.gov/research/programs/chords.
Landau WM (2021). “The targets R package: a dynamic Make-like function-oriented pipeline toolkit for reproducibility and high-performance computing.” Journal of Open Source Software, 6(57), 2959. https://doi.org/10.21105/joss.02959.
Manware M, Song I, Marques E, Alifa Kassien M, Messier K (2024). amadeus: Accessing and Analyzing Large-Scale Environmental Data. R package version 1.2.0, https://niehs.github.io/amadeus/.
Messier KP, Katzfuss M. Scalable penalized spatiotemporal land-use regression for ground-level nitrogen dioxide. Ann Appl Stat. 2021 Jun;15(2):688-710. doi: 10.1214/20-aoas1422. Epub 2021 Jul 12. PMID: 35069963; PMCID: PMC8774268.
*Email: mariana.kassien@nih.gov. Abstract number 1649325
Notes: References – Kyle 2021 paper